## Slide 1: HOW TO POWER YOUR RADIO WHEN THE LIGHTS GO OUT
Batteries, solar panels, and charge controllers

## Slide 2: Highly Condensed Version of a Six Hour Workshop
Vast majority of this information comes from Mark Breakey, KB7RHI, at the Friday Workshop at SeaPac 2019
Links to his material:
  http://www.seapac.org/workshop-presentations_files/SEA-PAC2019-batteries-kb7rhi.pdf
  http://www.seapac.org/workshop-presentations_files/SEA-PAC2019-solar-panels-kb7rhi.pdf
  http://www.seapac.org/workshop-presentations_files/SEA-PAC2019-solar-controllers-kb7rhi.pdf

## Slide 3: Batteries
Two Basic Types in Wide Use Today
  Lead Acid Technologies
    Wet Cell or Flooded
    Gel Cell or Sealed
    AGM
  Lithium Iron Phosphate/Lithium Ferrous Phosphate (LFP)

## Slide 4: Pros and Cons of Lead Acid Batteries
Advantages
  Widely Available
  Will probably survive an EMP event
  “Cheaper”
Disadvantages
  MUST be stored in fully charged condition
  Heavy
  Long-term storage temperature greatly affects capacity
  Shorter life even when cared for well
  Extremely shorter life span if abused
  Longer, more complicated charge times
  Flooded type can be dangerous
    Spills
    Off gassing hydrogen when charging

## Slide 5: Types of Lead Acid Batteries
Starting Batteries
  Designed to delivery a heavy load for a very short period of time
  Easily damaged if drained too heavily
    Designed for only a 20% discharge
  Use only in an emergency when nothing else is available
Marine Batteries
  A compromise
Deep Cycle Batteries
  Designed to put out a rated amperage over a period of time and be recharged many times

## Slide 6: Characteristics of Deep Cycle Lead Acid Batteries
Voltage drops as battery discharges
  C rate is critical
    A battery is not like a bucket of water that you can just fill and/or drain as fast as you can
    A 100 amp hour battery handling a 100 amp load will last about 15 minutes
    Same battery handling a 5 amp load will go about 20 hours.
  NEVER let the battery drop below 50% of full charge
    AGMs are especially sensitive to this
    Voltage becomes unusable for most transceivers at 11.7 volts UNDER LOAD
      Battery starts at 12.7 volts and hits 11.7 at about 50% charge, again under load

## Slide 7: Characteristics of Deep Cycle Lead Acid Batteries (cont’d)
Depth of discharge and speed of charging drastically affect life span
  Again, AGMs are especially susceptible to this
    50% discharge = 400 cycles
    100% discharge = 4 cycles
  Charging process is complicated, takes a long time, and managed by the charger
    Three stage process
      Bulk—constant amperage
      Absorption—constant voltage
      Float—constant trickle voltage

## Slide 8: Wiring and voltage drop
Basically a one-volt window on a lead acid battery
  Wiring size and length can narrow that window considerably
    See Workshop slides for calculations
      Basically, keep the lengths short and the wire heavy
  Limit your peak transmitting load to 20% of your battery amp hour capacity.

## Slide 9: Pros of LFP Batteries
Pros
  Much higher energy density, i.e. roughly a quarter of the weight at the same power capability
  Stable chemical compounds = safe
  Basically can be discharged 100% with no damage
  Voltage curve is essentially flat until 90% discharged so more usable power e.g. 30 ah LFP = 55 ah AGM
  Longer life—2,000 recharge cycles typical
  Can provide sustained high current discharges with no damage
  Efficient (95% vs 85% for lead acid)
  Fast charging and no problem with partial charges or storing without recharging
  Chargers are dead simple because all the “brains” are built into the battery and battery will not allow over discharge or over charge
  Wide temperature range with no loss of performance

## Slide 10: Cons of LFP Batteries
More expensive

## Slide 11: Solar Panels
Covering only portable setups for field operation
  Lots of info on larger scale installations available
    Friend and former neighbor of mine in California gets a check back from the utility company for $100-$200 most months
  Cost of solar has dropped dramatically
    1975 = $101.05 per watt
    2017 = $0.53 a watt
    Both based on large grid tie installations
    Portable panels about $1.25 to $1.50 a watt today

## Slide 12: Characteristics of Solar Panels
Number of cells determines voltage
Size of cells determines amperage
Most portable panels are 36 cells yielding about 18 volts under load in bright sunlight
Lots of information on how solar cells create electricity from sunlight in his presentation

## Slide 13: Things to Remember about Solar Panels
Ratings are based on Standard Test Conditions (STC) and will never be realized in the real world
  Even though full sun on a mid latitude state in the US gets about 1,000 watts of sunlight per square meter, the max a panel could capture of that is about 200 watts
  Northern latitude states (like WA) get less (and drops DRAMATICALLY above about 60 degrees latitude and especially in the winter) but higher altitudes get more (less air to go through)
  Higher temps bring down power (via lowered voltage)
  Light levels impact power production greatly (but not voltage much)
  Cell materials vary widely in their ability to produce power
  Shade and dirt are your enemy
  New PTC ratings are more realistic

## Slide 14: Types of Solar Cells
Monocrystalline
  Most efficient
  Long lasting (some from the seventies still producing power at over 80% of rated power)
Polycrystalline
  Slightly less efficient (still not bad for portable use)
Thin film or amorphous
  HEAVY
  Less efficient
  Harbor Freight sells these
  Shorter life

## Slide 15: Connecting Solar Panels Together
Parallel
  Current is the sum of all the panels
  Voltage is the voltage of the lowest voltage panel connected
Series
  Voltage is the sum of all the panels
  Current is the current of the lowest voltage panel connected

## Slide 16: Size of Solar Panels for Field Use
40-120 watt panels are a good choice
  Small enough to be easily handled and placed
  Just parallel them together to create more power
    Example: Bioenno 120 folding panel is two 60-watt panels wired in parallel

## Slide 17: Miscellaneous Thoughts on Solar Panels
As with most things, you generally get what you pay for
Renogy and Bioenno both make solid panels
If you need 24 volts for POE for a small 2.4/5.8 gHz node, just use the Bioenno and reconnect the panels in series (just remember to use a 24-volt controller and a 24-volt battery pack)
Remember that 18-volt output under load for a 36-cell panel; we’ll come back to that when we talk about controllers
Lots and lots of good information in the linked presentation

## Slide 18: Charge Controllers
Charge controllers basically have one job: Control the voltage that goes to the battery
  Some, however, do add some bells and whistles to that job
Most controllers are battery technology specific
  LFP
  Lead acid
    Flooded
    AGM
    Gel
A few are designed to manage some/all
Rated by both voltage and amperage they will handle

## Slide 19: Connecting Up the Panel, Controller, Battery, and Load
Use a distribution block
  Order for connections to the block
    Battery
    Charge controller to the battery
    Charge controller to the panel
    Load (radio/whatever)
MC4 vs Anderson Power Poles
  MC4 rated for 20 amps at 600 volts but not rated for connect/disconnect under load
  Power Poles are rated for 100,000 no load connections and 250 under full load
  If using MC4s, connect them to the Power Poles first before connecting anything else
Keep charge controllers well away from flooded lead acid batteries
Find other uses for the power from the panel if batteries go into absorption mode/are fully charged in the middle of the day

## Slide 20: Types of Charge Controllers
On/Off (least efficient)
  Simple cut in and cut out voltage set points
Pulse Width Modulation (PWM)
  Uses short pauses in charge current to top off the battery
  Three stage charging
Maximum Power Point Tracking (MPPT) (most efficient)
  Converts voltage down to lower battery voltage
  Increases amperage during bulk charging
  Can be VERY RF noisy if not specifically designed to be quiet

## Slide 21: MPPT Controllers
“Buck” the voltage down to the battery voltage while increasing the amperage
  Convert DC to AC, transform voltage, convert back to DC
  5.5 amps at 18 volts become about 7 amps at 13 volts
“Boost” controllers do the reverse by raising low voltage up to battery voltage when light conditions aren’t good
  Most “buck/boost” controllers work down to about 9 volts input
RF quieter models include
  Genasun branded models
    GV-10 or GV-5 are a pretty good sizes for field radio use
    All are battery technology specific
  DIY Solar 4 U “Apollo” 16 amp and “Sol” (buck/boost) 20 amp (Sol is compatible with all technologies
    Owner is a ham radio operator
  Probably others

## Slide 22: MPPT Controllers (cont’d)
West Mountain Radio Epic Powergate
  Complete backup power system
    Solar charge controller
    Battery charging
    Works off normal power supply if available
    Radio never knows the power went out
    Rated up to 40 amp load
    Can handle up to 30 volts and 10 amps of solar panel input
    Works AGM, Gel, and LFP technologies
    RF noisy 

## Slide 23: Final Thoughts
In emergencies you could use
  Car batteries
  Home solar panels
    BE CAREFUL: home solar systems are wired in series and can carry 600 to 1,000 volts in the array
    Use only one panel disconnected from the array
      310 watts
      20 volts
      Make sure the controller and batteries can handle the amperage
Use voltage/amperage/watt hour meters
  They’ll tell you a lot about how your system is working
Go through the presentation from SeaPac; lots and lots of good information